## Slide 1: Homework 1

## Slide 2: Homework 1
Subject :
  Data Preprocessing
Description
  The raw data are often loosely controlled, resulting in out-of-range values, missing values, etc. The data preprocessing is an important step in the data mining process to quality of data. In this homework, you need to use R programming language to implement this process.
Data:
  The data of air quality from EPA
    http://taqm.epa.gov.tw/taqm/tw/default.aspx

## Slide 3: Homework 1
Step 1: Filter noise (abnormal) data
  E.g : out-of-range value

## Slide 4: Homework 1
Step 2. Fulfill missing value
  Use linear interpolation
  Linear interpolation is one of the technique to deal with missing values.
    linear interpolation takes two data points, say (xa,ya) and (xb,yb), and the interpolant is given by

## Slide 5: Homework 1
Air Quality Index (AQI)
  Taiwan
  The index is based on the concentrations of 6 pollutants. The index is calculated from the concentrations of the following pollutants: O3, PM2.5, PM10, CO, SO2andNO2. The breakpoints between index values are defined for each pollutant separately and the overall index is defined as the maximum value of the index. Different averaging periods are used for different pollutants.
Ref: https://taqm.epa.gov.tw/taqm/tw/b0201.aspx

## Slide 6: Homework 1
AQI |  |  |  |  |  |  | 
AQI | O3 (ppm) 8 hours mean | O3 (ppm) 1 hour mean | PM2.5 (μg/m3 ) 24 hours mean | PM10 (μg/m3 ) 24 hours mean | CO (ppm) 8 hours mean | SO2 (ppb) 1 hour mean | NO2 (ppb) 1 hour mean
0～50 | 0.000 - 0.054 | - | 0.0 - 15.4 | 0 - 54 | 0 - 4.4 | 0 - 35 | 0 - 53
51～100 | 0.055 - 0.070 | - | 15.5 - 35.4 | 55 - 125 | 4.5 - 9.4 | 36 - 75 | 54 - 100
101～150 | 0.071 - 0.085 | 0.125 - 0.164 | 35.5 - 54.4 | 126 - 254 | 9.5 - 12.4 | 76 - 185 | 101 - 360
151～200 | 0.086 - 0.105 | 0.165 - 0.204 | 54.5 - 150.4 | 255 - 354 | 12.5 - 15.4 | 186 – 304 | 361 - 649
201～300 | 0.106 - 0.200 | 0.205 - 0.404 | 150.5 - 250.4 | 355 - 424 | 15.5 - 30.4 | 305 – 604 | 650 - 1249
301～400 | (2) | 0.405 - 0.504 | 250.5 - 350.4 | 425 - 504 | 30.5 - 40.4 | 605 – 804 | 1250 - 1649
401～500 | (2) | 0.505 - 0.604 | 350.5 - 500.4 | 505 - 604 | 40.5 - 50.4 | 805 – 1004 | 1650 - 2049
actual
data

## Slide 7: Homework 1
Score
  1. Filter Noise data 10%
  2. Fulfill missing value 15%
    Please consider all possible cases
      E.g : Cross-day
  3. Calculate AQI of every hour (2nd day). 75%
    Each air pollutants (O3(8hour), O3(1hour), PM2.5, PM10, CO, SO2 and NO2) 70% (IAQIp)
    Find the maximum value of the index 5% (AQI)

## Slide 8: Homework 1
Input :
  A csv file (input.csv)
    The data of air quality from EPA
Output:
  The AQI and IAQIp of every hour.
    Format : Date, Hour, AQI, O3(8hour), O3(1hour), PM2.5, PM10, CO, SO2, NO2
      save as csv file (output.csv)

## Slide 9: Homework 1
Example:
output
input
…

## Slide 10: Deadline
Deadline
  2019/04/12 23:59
Submit
  Portal
Filename
  s+SID_HW1.r
    e.g : s1001234_HW1.r

## Slide 11: Bonus
Bonus 1 : Top 10% submit
  Note : Score > 90
Bonus 2 : Provide Data
  mailto: tinin@saturn.yzu.edu.tw